Tetra Tech, Inc.

# 3746 Mt. Diablo Boulevard - Suite 300

Lafayette, California 94549-3681

Telephone: (925) 283-3771

Telefax: (925) 283-0780

email:  claycreager@cs.com

To:		Suesan Saucerman

From:		Gary Wortham, Su Joy Roy, and Clayton Creager

Date:		April 12, 2001

Subject:	Draft Findings and Recommendations for EPA Region 9 Nutrient Criteria Project

The purpose of this memorandum is to provide the Regional Technical Advisory Group (RTAG) with an update on the development of Regional recommendations for nutrient criteria.  The first section of this update provides a summary of analyses of the bioassessment / water quality data received from Arizona Department of Environmental Quality.  The second section of this update includes a discussion of lessons learned from the pilot projects and provides recommendations for RTAG consideration regarding future efforts to develop nutrient criteria for the Region.

# Summary of Analysis of ADEQ Bioassessment Data for Rivers and Streams

Following the recommendation of the RTAG to investigate bioassessment data for the purposes of developing nutrient criteria, Tetra Tech contacted members of state and local agencies in EPA Region IX to obtain as much relevant data as possible.  Most people contacted had been referred to us as being involved in the collection of bioassessment data in Region IX.  The people contacted and results of this effort are summarized in Table 1.

In brief, it appears that although many agencies have initiated bioassessment programs recently, there is relatively limited data from Region IX that is available to us.  In particular, we need data with biological and co-located measurements of various chemical parameters.  Data meeting these requirements were hard to find.  To date, the only comprehensive dataset that we have been able to obtain is from the Arizona Department of Environmental Quality, where a five-year record of biology and chemistry is available from a number of stream monitoring stations.  We have therefore used these data to assess the usefulness of biological information for determining nutrient criteria across a wide region.

# Summary of data analysis

Benthic macroinvertebrate data and associated chemistry (nutrients, major ions, and selected trace metals) data were collected by Arizona DEQ from 1992-97.   Data were collected from several hundred stream stations and from different elevations. Macroinvertebrate data in the database were then used to calculate the metrics in Table 2.  Two separate indices were derived for low elevation (warm water) and high elevation (cold water) stations.  The indices use a subset of the entire list of candidate metrics that show the most differences between stations in reference and impacted streams.

We used all the available candidate metrics (not only those that were part of the Arizona indices), and co-located measurements of total Kjeldahl nitrogen and total phosphorus to find  relationships using simple x-y plots.  Such relationships, if robust, can be used in other areas, or can be used as a basis for collecting additional data. Because the bioassessment performed for Arizona DEQ divided the data into two groups (coldwater and warmwater), we made plots separately for the two groups of stations.  Plots of the candidate metrics with total phosphorus (TP) and total Kjeldahl nitrogen (TKN) appear in the attached Appendix.

Table 2: Attributes of benthic macroinvertebrates used as candidate metrics.  Modified from EPA Rapid Bioassessment Protocol: http://www.epa.gov/owowwtr1/monitoring/rbp/index.html

| Category | Metric | Definition | Predicted response to increasing perturbation |
| --- | --- | --- | --- |
| Richness measures | Total No. taxa | Measures the overall variety of the macroinvertebrate assemblage | Decrease |
|  | No. Diptera taxa | Number of "true" fly taxa, which includes midges | Decrease |
|  | No. EPT taxa | Number of taxa in the insect orders Ephemeroptera (mayflies), Plecoptera (stoneflies), and Trichoptera (caddisflies) | Decrease |
|  | No. Chironomidae taxa | Number of taxa of chironomid (midge) larvae | Decrease |
|  | No. Ephemeroptera Taxa | Number of mayfly taxa (usually genus or species level) | Decrease |
|  | No. Plecoptera Taxa | Number of stonefly taxa (usually genus of species level) | Decrease |
|  | No. Trichoptera Taxa | Number of caddisfly taxa (usually genus or species level) | Decrease |
| Composition Measures | % EPT | Percent of the composite of mayfly, stonefly, and caddisfly larvae | Decrease |
|  | % Plecoptera | Percent of stonefly nymphs | Decrease |
|  | % Trichoptera | Percent of caddisfly larvae | Decrease |
|  | % Diptera | Percent of all "true" fly larvae | Increase |
|  | % Chironomidae | Percent of midge larvae | Increase |
|  | % Ephemeroptera | Percent of mayfly nymphs | Decrease |
| Tolerance/Intolerance measures |  |  |  |
|  | No. of Intolerant Taxa | Taxa richness of those organisms considered to be sensitive to perturbation | Decrease |
|  | Hilsenhoff Biotic Index | Uses tolerance values to weight abundance in an estimate of overall pollution. Originally designed to evaluate organic pollution | Increase |
|  | % Tolerant Organisms | Percent of macrobenthos considered to be tolerant of various types of perturbation | Increase |
| Feeding measures | % Dominant Taxon | Measures the dominance of the single most abundant taxon. Can be calculated as dominant 2, 3, 4, or 5 taxa. | Increase |
|  | % Filterers | Percent of the macrobenthos that filter FPOM from either the water column or sediment | Variable |
|  | % Grazers and Scrapers | Percent of the macrobenthos that scrape or graze upon periphyton | Decrease |
| Habit measures | Number of Clinger Taxa | Number of taxa of insects | Decrease |
|  | % Clingers | Percent of insects having fixed retreats or adaptations for attachment to surfaces in flowing water. | Decrease |
|  | % Omnivores and Scavengers | Percent of generalists in feeding strategies | Increase |
|  | % Ind. Gatherers and Filterers | Percent of collector feeders of CPOM and FPOM | Variable |
|  | % Predators | Percent of the predator functional feeding group. Can be made restrictive to exclude omnivores | Variable |
|  | % Shredders | Percent of the macrobenthos that "shreds" leaf litter | Decrease |
|  | % Gatherers | Percent of the macrobenthos that "gather" | Variable |

# Findings

An analysis of the plots in the Appendix indicates that the majority of the candidate metrics do not show a clear response to nutrient concentrations.  A few metrics do show a limited response to nutrient chemistry, but the data appear to be too variable to discern a nutrient criterion.  There are several reasons for this finding as listed below:

- Stations used in this study were not designed specifically for evaluating nutrient impacts and the biological measurements may therefore reflect other, non-nutrient impacts, such as sediments;

- Biological measurements integrate the effects of chemistry over a period of time, but the point chemical measurements used in our analysis may contain enough short-term variability to mask the long-term effects;

- Range of nutrient concentrations encountered at these sites may not be wide enough to demonstrate clear changes.

It is possible that bioassessment data may be useful in identifying nutrient criteria concentration values.  However, the current data and analysis does not provide any evidence that would support specific recommendations for criteria.

# Lessons Learned – Outline for a Long-Term Strategy

## The EPA Region 9 Nutrient Criteria Project has tested two different assessment approaches using existing data to develop nutrient criteria recommendations for EPA Region 9.  It is clear from these pilot projects that there are substantial deficiencies in the available water quality monitoring data to support the development of nutrient criteria.  However, there are many valuable lessons learned from the pilot projects that can be used to guide future efforts to develop nutrient criteria in EPA Region 9.  This section of the update presents a series of recommendations to be considered by the RTAG for a framework to guide the collection and analysis of water quality information to achieve the objective of nutrient criteria that have been tailored to address the unique conditions of ecoregions within EPA Region 9.

## The EPA Region 9 Nutrient Criteria Project has been collecting existing water quality data throughout the Region to develop a database that can be assessed to determine nutrient criteria for several waterbody types.  The project has worked with the Regional Technical Advisory Group to collect information and to develop specific technical approaches to analyze the water quality data that was collected.  The project has determined that existing water quality data sets are not adequate to develop draft recommendations for nitrogen and phosphorus for EPA Region 9.  The Regional Technical Advisory Committee should acknowledge the long-term nature of their objective.  The results to date would suggest that the RTAG should develop a framework to support a long-term strategy for the development of nutrient criteria.  Included below are few preliminary recommendations that if adopted could provide the RTAG with the necessary focus and direction to begin collecting the necessary information and to develop a database to support the analyses required for the development of nutrient criteria for all relevant waterbody types for all ecoregions within EPA Region 9.

It is clear that many entities within EPA Region 9 are beginning monitoring programs that will collect the information that is needed to support nutrient criteria development.  What is needed is a coordinated information collection capability and a clear strategy for using the assembled information.  The outline of one possible strategy is offered below.

The strategy is based on the identification of a specific set of hypotheses for the development of nutrient criteria

The strategy includes the following steps:

- The RTAG develops specific nutrient criteria development hypotheses for each waterbody type within EPA Region 9 ecoregions (see example below).

- Define the minimum amount of information necessary to test each hypothesis.

- Use the RTAG as a forum to identify waterbodies throughout the Region where  water quality data (existing and future monitor efforts) will be collected to test the hypotheses.

- Write a work plan for each hypothesis that lists the candidate waterbodies and assignments for collecting the water quality data.

- Develop a web-based reporting database system that allows for information to be logged in from remote locations throughout the region.  A database administrator will update the access files after verifying each new entry.

The strategy will require the ongoing participation and coordination by EPA Region 9 to compile the information collected by participating entities throughout the Region.  The work plan and monitoring commitments could be updated as required.  However, candidate waterbodies identified by participants would where possible already be included in an ongoing monitoring program.  For example, several rivers on the North Coast of California are being monitored as part of TMDL implementation plans or as part of Endangered Species Act Habitat Conservation Plans.  Work plans for each ecoregion and waterbody type would include the RTAG approved hypothesis, information goals, a list of reporting waterbodies and the responsible agency, an analysis plan, and a schedule for development of criteria recommendation.  The centralized database allows participants to easily pass along information as it becomes available and to evaluate progress towards information objectives.

Example Hypothesis:  Rivers and Streams for all ecoregions:

The physical characteristics of unimpacted watersheds (such as land cover, land use, slope, stream habitat condition) can be defined that provide reference nutrient conditions for the waterbody.  It is possible to identify a group of reference condition monitoring stations that can provide reference concentrations for phosphorus and nitrogen.

Information needs:  40 stations for each ecoregion with good geographic distribution  (i.e., Ecoregion 2:  North Coast, Sierras, Central Coast, Arizona mountains).  Station watersheds will be characterized for all physical parameters used to define reference conditions.  Quarterly Water quality samples for two-years.  Biological assessment data collected for selected metrics.

Work Plan:  ADEQ – several streams from bioassessment monitoring program, USFS for streams included in salmon recovery program, USGS long-term monitoring stations, Regional Boards trend stations.  Contact information, existing monitoring protocol, analytical techniques, etc.

Schedule for completion:

### Other Hypothesis Concepts for Consideration

                - A hypothesis could be based robust query of the entire water quality dataset for a waterbody type within an ecoregion.  The evaluation of the entire distribution where a criteria concentration is selected from some point within the distribution is similar to the default approach identified in the National Criteria Development Documents.

                - The original strategy for Rivers and Streams creating a reference database of relatively unimpacted waterbodies that used existing data with comparison to a general population to help locate the criterion concentration point on the distribution.

                - The Arizona streams bioassessment strategy with greater attention to the development of the database (e.g., broader range of concentrations, seasonal sampling).

                - Others nominated by the RTAG.

These recommendations are made to provide a starting point for RTAG discussions as they begin to develop a long-term strategy for the development of nutrient criteria.